## Slide 1: Position Statement on Sealed Truss Placement Diagrams for the 2012 or 2015 International Building Code
Overview
Revised 3/22/2017

## Slide 2
SBCA has been the voice of the structural building components industry since 1983, providing educational programs and technical information, disseminating industry news, and facilitating networking opportunities for manufacturers of roof trusses, wall panels and floor trusses. SBCA endeavors to expand component manufacturers’ market share and enhance the professionalism of the component manufacturing industry.
Copyright © 2017 Structural Building Components Association.

## Slide 3: Introduction
Do Truss Designers have the responsibility to seal a Truss Placement Diagram (TPD)?
Short answer: NO

## Slide 4: Why not seal TPDs?
All necessary engineering design information is found on the Truss Design Drawings (TDD)
If Truss Design Engineers were to seal a TPD, they could inappropriately be held responsible for ensuring the proper flow of loads through the structure to the foundation.

## Slide 5: Why not seal TPDs?
Compare a truss to a window: both are manufactured and in turn installed within a building.
A window may be a highly engineered component of a house with specific installation specifications and instructions.
However, there is no requirement to provide an engineer’s seal on the installation instructions for windows.

## Slide 6: Purpose of TPDs
To assist the builder in positioning or locating the trusses and components supplied by the manufacturer.
To serve as detailed installation instructions
To indicate the manufacturer’s assumed location for each truss and component

## Slide 7: Background
The code language regarding Truss Placement Diagrams in the 2012 and 2015 IBC was introduced in the 2006 IBC code change process (S165-04/05).
The proposal was intended to improve clarity in terminology and included only a definition of a TPD :
  2303.4.2 Truss placement diagrams. Diagrams supplied by the truss manufacturer that identify the individually designated truss design drawings do not require the seal of a truss design engineer.

## Slide 8: Background
The proposal was modified during the 2006 IBC hearing process as follows:
  2303.4.1.3 Truss Placement Diagram. The truss manufacturer shall provide a truss placement diagram that identifies the proposed location for each individually designated truss and references the corresponding truss design drawing. The truss placement diagram shall be provided as part of the truss submittal package, and with the shipment of trusses delivered to the job site. Truss placement diagrams shall not be required to bear the seal or signature of the truss designer.
  Exception: When the Truss Placement Diagram is prepared under the direct supervision of a registered design professional, it is required to be signed and sealed.

## Slide 9: Background
In the 2009 IBC the definition of a TPD was revised again (S217-07/08) as proposed by the National Council of Structural Engineers Associations (NCSEA):
  2303.4.2 Truss placement diagram. The truss manufacturer shall provide a truss placement diagram that identifies the proposed location for each individually designated truss and references the corresponding truss design drawing. The truss placement diagram shall be provided as part of the truss submittal package, and with the shipment of trusses delivered to the job site. Truss placement diagrams that serve only as a guide for installation and do not deviate from the permit submittal drawings shall not be required to bear the seal or signature of the truss designer.

## Slide 10: Background
The rationale for the change proposed by S217-07/08 is as follows:
  The truss placement diagram is an erection diagram that replicates the information on the approved construction documents per Section 106.3. As it requires no engineering input, direct supervision and the signature and seal of a registered design professional is not required.

## Slide 11: Analysis – IBC
The 2012 and 2015 IBC include the following relevant sections that lay out the differences between TDDs and TPDs:
2303.4.1.4.1 Truss design drawings
2303.4.2 Truss placement diagram
2303.4.3 Truss submittal package

## Slide 12: Analysis – IBC
The 2012 and 2015 IBC Section 107 provide that the plans and specifications for a project shall be prepared by a licensed architect or engineer where required by the law of the jurisdiction in which the project is being constructed.
The plans and specifications should in turn clearly define the scope of the work proposed by the Building Designer.
107.1 General
107.2.1 Information on construction documents

## Slide 13: Analysis – Statutes for Professional Engineering
A state’s professional engineering law(s) and the IBC provide the basis upon which to evaluate the need to provide an engineer’s seal on a TPD.
Requiring the TPD to be sealed, where it is not prepared by an engineer or under his/her immediate personal supervision, is contrary to most state engineering laws which typically include language regarding sealing construction documents.
Based on the above, a TPD does not require a professional engineer’s seal for any building project in jurisdictions with similar statutes.

## Slide 14: Analysis – ANSI/TPI 1
ANSI/TPI 1, referenced by both the 2015 (14) and 2012 (07) IBC, clearly states that TPDs do not require an engineer’s seal when they serve only as a guide for Truss installation
The commentary further explains the intent of the standard
2.3.6.4 Truss Placement Diagram. …When the Truss Placement Diagram serves only as a guide for Truss installation and requires no engineering input, it does not require the seal of any Truss Design Engineer or Registered Design Professional.

## Slide 15: Analysis – ANSI/TPI 1
The Truss Designer’s sole responsibility is to design the individual trusses according to information provided by the RDP or Building Designer
The Truss Designer is therefore specifically responsible for the single truss design depicted on each TDD.

## Slide 16: Analysis – ANSI/TPI 1
TPDs are typically prepared by component manufacturer personnel other than Truss Designers.
The TPDs may not be reviewed or even seen by the Truss Designer.
It is therefore understood that TPDs are not prepared under the Truss Designer’s direct supervision.

## Slide 17: Findings
The 2012 and 2015 IBC Section 2303.4.2 both specify that a TPP does not require the seal of the truss designer when the TDD serves as a guide for installers.
It is the responsibility of the Building Designer to review the TPD, if provided, and verify that it does not deviate from the permit submittal documents.

## Slide 18: Conclusion
Truss Design Engineers should NOT be asked by RDPs, Building Designers or Building Code Officials to seal TPDs.

## Slide 19: References
ANSI/ TPI, National Design Standard for Metal Plate Connected Wood Truss Construction, Truss Plate Institute, 2007, 2014
International Building Code, International Code Council, 2006, 2009, 2012, 2015